## Slide 1: {SECTION TITLE}
STEPS:
VIDEO
{HEAD}
{STEPS}

## Slide 2: SECTION 1 - STEP 1 ----------------------------------- PLACEMENT AND SETUP
STEPS:
VIDEO
(SERVICE BOX SETUP) SEC 1 STEP 1
Place the populated Service Box with the labels facing you on the work-station using a construction screw.

## Slide 3: SECTION 1 - STEP 2 ----------------------------------- WIRE SETUP
STEPS:
VIDEO
(SERVICE BOX SETUP) SEC 1 STEP 2
Unscrew the service box screws half-way.

## Slide 4: SECTION 2 - STEP 1 ----------------------------------- CUTTING 6 AWG WIRES
STEPS:
VIDEO
(WIRE PREP) SEC 2 STEP 1
Cut the 6 AWG Green wire to 4.5 inches, the 6 AWG Red wire to 9.5 inches, and the 6 AWG Black wire to 6.5 inches

## Slide 5: SECTION 2 - STEP 2 ----------------------------------- CUTTING 8 AWG WIRES
STEPS:
VIDEO
(WIRE PREP) SEC 2 STEP 2
Cut 4 count 8 AWG Black wire to 7 inches,10 inches,11.5 inches,12 inches, the 8 AWG Red Wire to 11 inches,13.5 inches.

## Slide 6: SECTION 2 - STEP 3 ----------------------------------- STRIPPING WIRES
STEPS:
VIDEO
(WIRE PREP) SEC 2 STEP 3
Strip both ends of all wires Â½ inch, for the 8 AWG except Black , which should have one end stripped to 1 inch and the other to Â½ inch.

## Slide 7: SECTION 2 - STEP 4 ----------------------------------- SOLDER WRAPPING
STEPS:
VIDEO
(WIRE PREP) SEC 2 STEP 4
Wrap solder around the stripped ends of all the wires

## Slide 8: SECTION 2 - STEP 5 ----------------------------------- SOLDERING
STEPS:
VIDEO
(WIRE PREP) SEC 2 STEP 5
Solder all wire ends, ensuring no loose wire strands remain.

## Slide 9: SECTION 3 - STEP 1 ----------------------------------- 6 AWG
STEPS:
VIDEO
(WIRING CONNECTIONS) SEC 3 STEP 1
Starts with 6 AWG Green and goes from GB to NB. Then 6 AWG AWG Red and Black From 60A 2 Pole terminal Breaker to Block.

## Slide 10: SECTION 3 - STEP 2 ----------------------------------- 8 AWG
STEPS:
VIDEO
(WIRING CONNECTIONS) SEC 3 STEP 2
Connect the last 6 wires from 1,2 pole terminals to 30 , 15 A Breaker .

## Slide 11: SECTION 3 - STEP 3 ----------------------------------- LOCK TIGHT
STEPS:
VIDEO
(WIRING CONNECTIONS) SEC 3 STEP 3
Apply Lock Tight to all screws

## Slide 12: SECTION 3 - STEP 4 ----------------------------------- GUARDS
STEPS:
VIDEO
(WIRING CONNECTIONS) SEC 3 STEP 4
Add the guards to the pole terminal